ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 126

Date:	2000-02-08

Subject:	Power consumption of locally powered TE which draw power from the basic rate interface

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	TBR 3/A1 and TBR 33 both allow a power consumption of max. 3mW for locally powered TEs.

-	There are TEs which are locally powered but consume more than 3mW from the line (i.e. when using a connection detector).

Most public NTs in current installations offer 4W to 5W in normal mode.

In restricted mode a public NT offers 420mW.

A designated TE may consume 380mW in restricted mode.

ITAAB advises the following:

For a locally powered TE a power consumption of more than 3mW shall be allowed under the following prerequisites :

The manufacturer has to declare the power consumption in the manual of the TE.

The power drawn from the line shall be independent from the state of the TE and the voltage of the NT.

The TE may consume up to 380mW. The maximum number of TEs which are powered by the line has to be reduced by one. No designated TE may be connected at the bus.

The TE shall be tested as follows :

In the PICS/PIXIT parameter list LP, PS and DES shall be set to TRUE. A note shall be added and the maximum power consumption of the TE shall be declared.

Electrical tests and functional tests (B.2, B.3, B.4) shall be selected according to ITAAB Advisory Note 060 with LP set to TRUE and PS and DES set to FALSE. The test laboratory shall make sure that the test equipment offers the power needed by the TE.

For power consumption (B.5.1, B.5.2) the tests according to ITAAB Advisory Note 060 with LP set to TRUE shall be selected. The limit shall be changed to 380mW.

All other power feeding tests shall be selected according to ITAAB Advisory Note 060 with LP set to FALSE and PS and DES set to TRUE.
In test B.5.4.1 table 9.12 shall be used for both normal and restricted mode.