ITAAB

TRAC ISDN Type Approval Advisory Board

RECOMMENDATIONS FOR THE

ACCREDITED TESTING

AND TYPE APPROVAL OF

ISDN TERMINAL EQUIPMENT

ITAAB Permanent Reference Document:  IT.01

Version:	22

Date:	1998-10-19

Editor:	Chairman of ITAAB, G. Tind

Tele Danmark A/S, Research and Development

REFERENCE DOCUMENTS:

CTR 1	97/544/EC, Commission Decision of 9 July 1997

CTR 2	97/545/EC, Commission Decision of 9 July 1997

CTR 3 Amendment 1	98/515/EC, Commission Decision of 17 June 1998

CTR 4 Amendment 1	98/518/EC, Commission Decision of 17 June 1998

CTR 8	95/526/EC, Commission Decision of 28 November 1995

CTR 12 Amendment 1	97/520/EC, Commission Decision of 9 July 1997

CTR 13	97/521/EC, Commission Decision of 9 July 1997

CTR 14 Amendment 1	97/522/EC, Commission Decision of 9 July 1997

CTR 24	97/639/EC, Commission Decision of 19 September 1997

CTR 25	97/751/EC, Commission Decision of 31 October 1997

CTR 33	98/521/EC, Commission Decision of 17 June 1998

CTR 34	98/520/EC, Commission Decision of 17 June 1998

1.	GENERAL

1.1	Foreword

Type approval under the European Directive 91/263/EEC for connection of ISDN Terminal Equipment to EURO-ISDN was until November 1994 based on NET 3 part 1 and 2 for Basic Access, NET 5 for Primary Rate Access, and NET 33 for equipment supporting the 3,1 kHz telephony teleservice, when connected to an ISDN basic access.

At its meeting 1993-12-10, TRAC decided to set up an ad-hoc group, ISDN Type Approval Advisory Ad-Hoc Group, ITAAAG, to consider urgent problems derived from NET 3, NET 5 and NET 33, encountered during type approval or conformity assessment.

By the Commission Decisions 94/797/EC and 94/796/EC of 18 November 1994, Common Tecnical Regulations have come into force for access to the pan-European integrated services digital networks for basic and primary rate access. These CTR's are based on the tests defined in NET 3 and NET 5, and constitutes the so-called "ISDN Bridging Measures".

At its meeting 1994-06-01 and 1994-06-02, TRAC decided to extend the Terms of Reference for ITAAAG to cover the "ISDN Bridging Measures", national variants related to these measures, as well as CTR 8.

Since the full NET 3 and NET 5 are no longer in force, ITAAAG decided at its meeting 1995-09-05 and 1995-09-06 that those parts of NET 3 and NET 5, which are not required to support Commision Decisions 94/797/EC and 94/796/EC will no longer be maintained.

By Commission Decision 95/526/EC of 28 November 1995, CTR 8 has come into force.

Since no problems have been reported for NET 33 at the date CTR 8 came into force, NET 33 will no longer be maintained.

At its meeting 1996-03-27 and 1996-03-28, TRAC decided that ITAAAG (if they wished) could be changed to the ISDN Type Approval Advisory Board, ITAAB. At its meeting 1996-04-16 and 1996-04-17, ITAAAG decided to change to ITAAB.

At its meeting 1996-06-04 and 1996-06-05, TRAC decided to extend the scope of work for ITAAB to cover also CTR 12, CTR 14 and the coming CTR 13.

By the Commission Decisions 97/346/EC and 97/347/EC of 20 May 1997, Common Tecnical Regulations based on TBR 3 and TBR 4 have come into force for access to the pan-European integrated services digital networks for basic and primary rate access.

By the Commission Decisions 97/520/EC, 97/521/EC and 97/522/EC of 9 July 1997, Common Tecnical Regulations based on TBR 12 as amended by TBR 12/A1, TBR 13 and TBR 14 as amended by TBR 14/A1 have come into force for attachment to the 2 048 and 64 kbit/s digital ONP leased lines. These Commission Decisions repeal CTR 12 and CTR 14 with effect from 9 July 1998.

At its meeting 1997-11-13 and 1997-11-14, TRAC decided to extend the scope of work for ITAAB to cover also CTR 1, CTR 2, CTR 24, CTR 25, CTR 33 and CTR 34.

Since the "ISDN Bridging Measures” in Commission Decisions 94/797/EC and 94/796/EC have expired on 20 May 1998, ITAAB decided at its meeting 1998-05-19 and 199-05-20 that those parts of the ISDN standards, which are not required to support the new Commision Decisions on ISDN will no longer be maintained.

By the Commission Decisions 98/515/EC and 98/518/EC of 17 June 1998, Common Tecnical Regulations based on TBR 3 as amended by TBR 3/A1, TBR 4 as amended by TBR 4/A1, have come into force for access to the pan-European integrated services digital networks for basic and primary rate access. These Commision Decisions repeal CTR 3 and CTR 4 with effect from 20 May 1998.

By the Commission Decisions 98/521/EC and 98/520/EC of 17 June 1998, Common Tecnical Regulations based on TBR 33 and TBR 34 have come into force for access to the packet mode pan-European integrated services digital networks for basic and primary rate access.

1.2	Participants in ITAAB

The participants in ITAAB are drawn from the following areas of expertise:

-	Administrations

-	Type Approval Authorities

-	Operators

-	Test Houses

-	Standards Institutes

-	ISDN Terminal Equipment Manufacturers

-	Test Equipment Manufacturers

1.3	Scope

This Permanent Reference Document (PRD) of the TRAC ISDN Type Approval Advisory Board (ITAAB) provides a reference list for the Advisory Notes, which are approved by the experts appointed as members of ITAAB, and applicable for type approval according to CTR 1, CTR 2, CTR 3 A1, CTR 4 A1, CTR 8, CTR 12 A1, CTR 13, CTR 14 A1, CTR 24, CTR 25, CTR 33 and CTR 34.

The objective of this PRD is to specify a common approach to the type-examination of Terminal Equipment according to these Type Approval specifications.

This PRD is advisory in nature, but compliance with the referenced Advisory Notes by type approval authorities should ensure an agreed common platform for the type examination of Terminal Equipment for attachment to ISDN and to digital lines, for which approval is covered by the reference CTR’s.

For reference purposes this PRD also provide a list of those Advisory Notes, which previously have been approved by ITAAB, but now are withdrawn. (This list does not provide information about latest approved version.)

1.4	Reference CTR’s

This document provides a reference list for the Advisory Notes issued by ITAAB, to be used by test houses and type approval authorities when assessing conformity of Terminal Equipment with the requirements found in CTR 1, CTR 2, CTR 3 A1, CTR 4 A1, CTR 8, CTR 12 A1, CTR 13, CTR 14 A1, CTR 24, CTR 25, CTR 33 and CTR 34.

The full titles of the CTR’s referenced by this PRD are:

CTR 1	97/544/EC, Commission Decision of 9 July 1997 on a common technical regulation for terminal equipment to be connected to the public switched data networks and ONP leased lines circuits using a CCITT Recommendation X.21 type interface

CTR 2	97/545/EC, Commission Decision of 9 July 1997 on a common technical regulation for the general attachment requirements for Data Terminal Equipment (DTE) to connect to Packet Switched Public Data Networks (PSPDNs) offering CCITT Recommendation X.25 interfaces

CTR 3 A1	98/515/EC, Commission Decision of 17 June 1998 on a common technical regulation for the pan-European Integrated Services Digital Network (ISDN) Basic Access (Amendment 1)

CTR 4 A1	98/518/EC, Commission Decision of 17 June 1998 on a common technical regulation for the pan-European Integrated Services Digital Network (ISDN) Primary Rate Access (Amendment 1)

CTR 8	95/526/EC, Commission Decision of 28 November 1995 on a common technical regulation for ISDN; Telephony 3,1 kHz teleservices, attachment requirements for handset terminals

CTR 12 A1	97/520/EC, Commission Decision of 9 July 1997 on a common technical regulation for the attachment requirements for terminal equipment interface for connection to 2 048 kbit/s digital unstructured ONP leased line (Amendment 1)

CTR 13	97/521/EC, Commission Decision of 9 July 1997 on a common technical regulation for the attachment requirements for the terminal equipment interface for connection to 2 048 kbit/s digital structured ONP leased line

CTR 14 A1	97/522/EC, Commission Decision of 9 July 1997 on a common technical regulation for the attachment requirements for the terminal equipment interface for connection to 64 kbit/s digital unstructured ONP leased line (first revision)

CTR 24	97/639/EC, Commission Decision of 19 September 1997 on a common technical regulation for the attachment requirements for the terminal equipment interface for connection to 34 Mbit/s digital unstructured and structured leased lines

CTR 25	97/751/EC, Commission Decision of 31 October 1997 on a common technical regulation for the attachment requirements for the terminal equipment interface for connection to 140 Mbit/s digital unstructured and structured leased lines

CTR 33	98/521/EC, Commission Decision of 17 June 1998 on a common technical regulation for ISDN packet mode using ISDN basic access

CTR 34	98/520/EC, Commission Decision of 17 June 1998 on a common technical regulation for ISDN packet mode using ISDN Primary Rate Access

2.	LIST OF ADVISORY NOTES APPROVED BY ITAAB

2.1	ISDN Basic and Primary Rate Access

| Advisory | Subject | Applicable for CTR |
| --- | --- | --- |
| Note No. |
| 3/A1 | 4/A1 | 8 | 33 | 34 |
| 048 rev. 2 | Handling of glitches when performing tests B.2.4 and B.2.6.1 of TBR 3 | X |
|  | X |
|  | 053 rev. 2 | TTCN description of preamble PRE_F3_CP | X |
|  | X |
|  | 054 rev. 3 | Additional French attachment requirements for ISDN | X | X |
| X | X |
| 055 | Value of state used in STATUS message | Note 1 | Note 1 |
|  | 060 rev. 1 | Testing to be performed for Basic Access layer 1, including variations of Power Sources to be applied during testing of Electrical Characteristics | X |
| 061 rev. 2 | Problem with performing the electrical characteristics tests at Basic Access Layer 1 for TEs with an unstable state F3 | X |
|  | X |
|  | 063 rev. 2 | Output jitter test of TBR 12 and TBR 13 |
|  | Note 2 |
| 066 rev. 2 | Test case selection to be performed for Basic Access and for Primary Rate Acess for layers 2 and 3 | Note 3 | Note 3 |
|  | 067 | Testing to be performed for Primary Rate Access layer 1 |
| Note 4 |
|  | 068 rev. 1 | CRC processing and generation of CRC error reports: Monitoring contiguous E bits |
| X |
|  | X |
| 069 rev. 1 | Basic Access Layer 1 tests with problems for unstable S4 at layer 2 | X |
|  | X |
|  | 070 rev. 1 | CRC processing Test Procedure change |
| X |
|  | X |
| 071 rev. 1 | Requirements to EURO-ISDN basic access terminal equipment capable of handling only incoming or only outgoing calls | X |
| 072 rev. 1 | Requirements to EURO-ISDN primary rate access terminal equipment capable of handling only incoming or only outgoing calls |
| X |
|  | 075 rev. 1 | Approval of TE’s capable of automatic inter-working between equipment with and without CRC-4 capability |
| X |
|  | X |
| 076 rev. 1 | Problem with performing the functional characteristics tests at Basic Access Layer 1 for TEs with an unstable state F3 | X |
|  | X |
|  | 079 | Total Delay in Terminal Equipment |
|  | X |
| 080 | Use of preferred/exclusive bit in the RESTART ACK PDU in TC19003 | Note 5 | Note 5 |
| Note 5 | Note 5 |
| 082 rev. 1 | Connection of the simulator to the IUT |
| X |
|  | X |
| 083 rev. 1 | Layer 3 default DF69901 | X | X |
|  | 084 rev. 1 | Layer 3 response time in layer 2 tests |
| X |
|  | X |
| 085 rev. 1 | Information element checking in layer 3 TC20002 | X | X |
|  | 086 rev. 1 | Layer 2 test case TC27031 | X | X |
| X | X |
| 087 | Handling of IUT’s supporting En-bloc sending without using the Sending Complete IE, or supporting more than one dialling mode | X | X |
|  | 088 rev. 1 | Postamble CHECK_F1 | X |
|  | X |
|  | 089 | Value of Listener Side Tone Rating (LSTR) |
|  | X |
| 094 | Timer TWAIT in the S0 Layer 1 Testsuite | X |
|  | X |

Note 1: Advisory Note 055 applies to CTR 3 and CTR 4, but is under revision to cover CTR 3/A1 and CTR 4/A1.

Note 2: Advisory Note 063 rev. 2 applies to CTR 12 and CTR 13, but is under revision to cover CTR 12/A1, CTR 13 and CTR 34.

Note 3: Advisory Note 066 applies to CTR 3 and CTR 4, but is under revision to cover CTR 3/A1 and CTR 4/A1.

Note 4: Advisory Note 067 applies to CTR 4, but is under revision to cover CTR 4/A1.

Note 5: Advisory Note 080 applies to CTR 3 and CTR 4, but is under revision to cover CTR 3/A1, CTR 4/A1, CTR 33 and CTR 34.

2.2	TE interface for ONP and digital leased lines

| Advisory | Subject | Applicable for CTR |
| --- | --- | --- |
| Note No. |
| 12/A1 | 13 | 14/A1 | 24 | 25 |
| 063 rev. 2 | Output jitter test of TBR 12 and TBR 13 | Note 6 | X |

Note 6: Advisory Note 063 rev. 2 applies to CTR 12 and CTR 13, but is under revision to cover CTR 12/A1, CTR 13 and CTR 34.

2.3	TE interface for V-series interfaces

| Advisory | Subject | Applicable for CTR |
| --- | --- | --- |
| Note No. |
| 1 | 2 |
| 090 | Testing for X.21 circuits | X | X |
| 091 | Data Rates for testing | X | X |
| 092 | TE with X.21 or X.21bis interfaces with one or more configurations which do not support X.25 |
| X |
| 095 | Test description for Receiver effective shunt capacitance for CCITT V.28 interchange circuits ( 7.5.2.1 ) |
| X |

3.	LIST OF WITHDRAWN ADVISORY NOTES

3.1	ISDN Basic and Primary Rate Access

| Advisory | Subject | Reason for withdrawal |
| --- | --- | --- |
| Note No. |
| 001 | SETUP message via point-to-point data link for TE in point-to-point configuration | Applied for NET 3 and “I-CTR 3” |
| 002 | Restart procedure for a TE in point-to-point configuration | Applied for NET 3 |
| 003 | Compatibility checking to be performed by an NT2 | Applied for NET 3 and “I-CTR 3” |
| 004 | Correction of editorial error in test 13.4.2 of ETS 300 104 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 005 | Correction of editorial error in test 8.10 of ETS 300 104 | Applied for NET 3 and NET 5 |
| 006 | Correction of editorial error in test 11.1 of ETS 300 104 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 007 | Test of Timer T303 | Applied for NET 3 and NET 5 |
| 008 | Definition of an undefined frame | Applied for NET 3 and NET 5 |
| 009 | Receipt of modulo 8 frame during modulo 128 operation | Applied for NET 3 and NET 5 |
| 010 | Correction of editorial error in test D.3.2.1 of ETS 300 012 concerning test state 46, Expiry of T3 in state F8 | Applied for “I-CTR 3” |
| 011 | Testing to be performed for Basic Access layer 1, including variations of Power Sources to be applied during testing of Electrical Characteristics | Applied for NET 3 and “I-CTR 3” |
| 012 | Frame Alignment procedure | Applied for NET 3 and “I-CTR 3” |
| 013 | Current/time limitation for TE when connecting | Was superseded by AN 011 |
| 014 | Voltage and current limitations under single fault conditions | Applied for NET 3 and NET 5 |
| 015 | Test Environment | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 016 | Correction of editorial errors in Clause A.2.2.4 of ETS 300 156 | Applied for NET 5 and “I-CTR 4” |
| 017 | Use of TEI values and TEI management procedures for Primary Rate Access | Applied for NET 5 and “I-CTR 4” |
| 018 | Safety and Protection requirements for "ISDN Bridging Measures" | Applied for “I-CTR 3” and “I-CTR 4” |
| 019 | References to TTCN Test Cases | Applied for "I-CTR 3", "I-CTR 4", CTR 3 and CTR 4 |
| 020 | Capability to enter state F5 on detection of "Any Signal" | Applied for NET 3 and “I-CTR 3” |
| 021 | Connection Detector for TEs of the Automatic TEI assignment category | Applied for NET 3 and “I-CTR 3” |
| 022 | Packet mode Terminals (TEs using SAPI = 16) | Not needed after CTR 33 and CTR 34 in force |
| 023 | Handling of MPH-EI1 primitive | Applied for NET 3 and “I-CTR 3” |
| 024 | Connection arrangements and related visual inspection | Applied for NET 3 and “I-CTR 3” |
| 025 | Ambiguity in layer 2 test A.2.2.4.5 | Applied for NET 5 and “I-CTR 4” |
| 026 | Precondition for test A.2.2.5.1 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 027 | Correction of editorial error in test 13.8 of ETS 300 104 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 028 | Use of TEI values and TEI management procedures for Basic Access | Applied for NET 3 and “I-CTR 3” |
| 029 | Upper Frequency for measurement of LCL | Applied for “I-CTR 3” |
| 030 | Measurement requirements and limits for Tolerable longitudinal voltage and Impedance to ground | Applied for “I-CTR 4” |
| 031 | CRC multiframe alignment | Applied for NET 5 and “I-CTR 4” |
| 032 | Time limits for Frame Alignment | Applied for NET 5 and “I-CTR 4” |
| 033 | Cause Information Element in DISCONNECT message from TE | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 034 | Problem with test A.2.2.1.4 in ETS 300 153 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 035 | Handling of test A.2.2.1.1 for a TE which is unstable in state 4 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 036 | Layer 2 processing time | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 037 | Problem with test A.2.2.3.1 in ETS 300 153 | Applied for NET 3, NET 5, “I-CTR 3” and “I-CTR 4” |
| 038 | Timers T305 and T308 | Applied for “I-CTR 3” and “I-CTR 4” |
| 039 | Testing to be performed for Basic Access layer 2 | Applied for “I-CTR 3” |
| 040 | Testing to be performed for Primary Rate Access layer 2 | Applied for “I-CTR 4” |
| 041 | Testing to be performed for Primary Rate Access layer 1 | Applied for “I-CTR 4” |
| 042 | Testing to be performed for Basic Access layer 3 | Applied for “I-CTR 3” |
| 043 | Testing to be performed for Primary Rate Access layer 3 | Applied for “I-CTR 4” |
| 044 | CRC processing and generation of CRC error reports | Applied for “I-CTR 4” |
| 045 | I-frame acknowledgement | Applied for "I-CTR 3", "I-CTR 4", CTR 3 and CTR 4 |
| 046 | Basic Access Layer 1 tests with problems for unstable S4 at layer 2 | Applied for “I-CTR 3” |
| 047 | Connection for testing of a TE capable of having a standard ISDN basic access cord connected | Applied for “I-CTR 3” |
| 049 | TTCN description of postamble CHECK_F1 | Applied for “I-CTR 3” |
| 050 | TTCN description of tests CPF6PHARa and CPF8PHARa | Applied for “I-CTR 3” |
| 051 | Description of PX_T_APPLI1 and PX_T_APPLI2 | Applied for “I-CTR 3” |
| 052 | Active Connection | Applied for CTR 3 |
| 057 | CRC processing and generation of CRC error reports | Applied for “I-CTR 4” |
| 058 | Value of the state used in STATUS message | Applied for “I-CTR 3” and “I-CTR 4” |
| 062 | Testing of Primary Rate Access Layer 1 State Matrix | Applied for “I-CTR 4” |
| 064 | Interframe (layer 2) time fill in the Belgium ISDN network provided by Belgacom | Applied for older versions of the Belgacom network |
| 074 | Tests for timers T305 and T308 | Applied for CTR 3 and CTR 4 |
| 081 | Incidental non-compliances | Applied for "I-CTR 3", "I-CTR 4", CTR 3 CTR 4 and CTR 8 |
| 093 | Error in Layer 2 test case TC27040 | Applied for CTR 3 and CTR 4 |

3.2	TE interface for ONP and digital leased lines

| Advisory | Subject | Reason for withdrawal |
| --- | --- | --- |
| Note No. |
| 073 rev. 1 | Connector Arrangement specified in TBR 12 and TBR 14 | Applied for CTR 12 and CTR 14 |