|  | ToR STF 453 ext (TC INT) |
| --- | --- |
|  | Version: 1.2 |
|  | Author: Giulio Maggiore – Date:08 August 2012 |
|  | Last updated by: Alberto Berrini – Date:25 September 2013 |
|  | page 1 of 7 |

Revised Terms of Reference - Specialist Task Force

STF 453 (TC INT)

”Update of IMS NNI and IMS&EPC Test Specifications 
to 3GPP R10 and RCS 5.0”

Summary information

| Approval status | Approved by TC INT and Board#90 (15-Nov-2012) Proposed extension 26 working days (incl. 20% volunt.) + 3 000 € travel = 15 480 € Status extension: for approval Board#94 (18-19 September 2013). |
| --- | --- |
| Funding | 70 280 € (54 800 € approved by Board#90 + 15 480 € extension request to Board#94) voluntary contribution 20% of total manpower |
| Time scale | Feb 2013 to Feb 2014 |
| Work Items | RTS/INT-00085-1, TS 186 011-1 V5.1.1 RTS/INT-00085-2, TS 186 011-2 V5.1.1 RTS/INT-00086, TS 102 901 V5.1.1 RTS/INT-00087, TS 103 029 V4.1.1 DTS/INT-00091, TS 103 189 |
| Funding criteria B(12)88_030 | 4. Standards enablers/facilitators (e.g. conformance test/interoperability). Strong support from Members of different categories (operators, vendors, R&D, academic) |
| Notes from TC INT | Update required to take into account feedback from manufacturers on the early draft produced by STF453. Modification needed to prepare interop event and validation for VoLTE into 2013. Work will be done under close CTI overview. |

Part I – Reason for proposing the STF

# Rationale

IMS is a key component in the upcoming VoLTE (Voice over LTE) and the EPC architecture and is already the corner stone for the 3GPP NGN and FMC architecture. Parts of EPC are already in implementation, but not yet for Voice. Associated with VoLTE roll out is the compatibility with RCS.

Equally important are the network-to-network interfaces (NNI), which are essential for a global migration to the new standards. A set of ETSI interoperability test specifications (TS 186 011- 3, TS 102 901, TS 103 029) already exists and will be used at the RCS VoLTE IOT 2012 co-organised by ETSI, GSMA and the MSF for 3GPP R9.

Regarding timing, it is also taken into consideration that the IOT event has a key role in providing feedback to 3GPP and to the industry before the start of GSMA demonstrations and Trials.

Therefore, the main objective of this STF is to update test specifications for conformance checks for 3GPP R10 NNI, Evolved Packet Core (EPC) use cases and RCS Release 5.0, leading to a strong collaboration between TC INT, 3GPP and GSMA IREG and RCS. The result of this collaborative work could be used in upcoming RCS VoLTE IOT events.

TC INT has identified a need for specific tests for:

Interoperability for 3GPP Release 10 on NNI

RCS Release 5.0

IMS and EPC Interworking for 3GPP Release 10

QoS for voice and video services for established connections

Moreover, the feedback from the validation phase of the current test specifications version could reveal some improvement areas that could be integrated in the scope of this STF.

This revision of STF453 proposes an extension of the QoS related work in order to revise TS 103 189 which contains the results of task T6 and which is ready for approval in September 2013. This revision will integrate feedback from test houses and the conclusions and results of a validation test planned by ETSI CTI for December 2013, see proposed new task T7. In addition ETSI CTI has requested a three day support by both QoS experts during the validation tests, see proposed new task T8.

Therefore, the following resources will be required in addition to those already planned:

For task T7:

Additional manpower: 9 600 EUR, corresponding to 20 working-days (including 20% voluntary contribution)

Travel expenses: 1 000 EUR

For task T8:

Additional manpower: 2 880 EUR, corresponding to 6 working-days (including 20% voluntary contribution)

Travel expenses: 3 000 EUR

There is a clear benefit in the extension of this STF since the revised QoS document can be much more comprehensive and complex by taking into account feedback and practical validation experience. It is urgent to do this work as soon as possible, because the enhanced document is required for the next VoLTE plugtest planned for 2014 and should be available well in advance before the event in order to implement all requirements properly.

# Objective

This STF will update and enhance the existing IMS NNI test specifications (deliverable of STF 414) and will synchronize its efforts with STF 450 and STF 445. Most of the updated test cases will be linked to services impacted by 3GPP Release 10 and RCS 5.0 use cases. Some minor updates might be required to TS related to the interface between IMS and EPC.

# Relation with ETSI strategy and priorities

This STF is directly related to ETSI strategic objective "Major Strategic Topics - NGN" and “Service level interconnection of IP-Based Services” and corresponds to the “Standards enablers/facilitators (conformance testing, interoperability, methodology)” category.

Moreover, the QoS related work (see Task 6) of the proposed STF relates directly to the subject of End to End QoS, one of the provisional list of strategic topics for 2009 contained in the ETSI Board report to GA#51.

# Context of the proposal

## ETSI Members support

| ETSI Member | Supporting delegate | Motivation |
| --- | --- | --- |
| Telecom Italia | Giulio Maggiore | Tests used to get detailed information from vendors about Interoperability Testing before coming to the market |
| Telekom Austria | Martin Brand | Tests needed for internal network testing |
| Deutsche Telekom | Gerhard Ott | Tests needed for internal network testing |
| AT&T | Dewayne Sennet | Tests used to promote conformance testing for Public Safety |
| Telekom Slovenjia | Matjaz.Bericic | Test used to promote interoperability among vendors |
| Cisco | Jesus Trujllo Gomez | Test will be used for quality enhancement of IMS product |
| ZTE | David Huo | Test will be used for quality enhancement of IMS product |
| Neustar | Andreas Roeth | Test to improve IMS Enabling solution |
| Iskratel | Primoz Svigeli | Test will be used for quality enhancement of IMS product |
| Italtel | Diego Saiu | Test will be used for quality enhancement of IMS product |
| Arcatech | Terence A, Simpson | Provide test system for functional and performance test. |
| Codenomicon | Ari Takanen | Provide test system to test protocols |
| Confomiq | Stephan Schulz | Generation of tests for testing protocol |
| Testing Tech | Theofanis Vassiliou-Gioles | Provide the Test System for the test cases implementation and execution |
| Fokus | Axel Rennoch | Research Institute, advanced automated/standardized test solutions with TTCN-3 |
| Technical University of Berlin | Julius Muller | Research Institute, EPC/NGN evolution |
| Elvior | Andres Kull | Tool Provider, Provide the Test System for the test cases |
| Mesaquin.com s.r.o. (Ltd) | Jan Holub, CEO | promoting QoS aspects for LTE |
| PQM Consultants | Joachim Pomy, QoS expert | promoting QoS aspects for LTE |
| University of Zilina | Peter Pocta Assistant Professor | promoting QoS aspects for LTE |

## Market impact

ETSI is creating a global IMS test standard and experience shows that interconnection tests of services is a basic component for its success. GSMA RCS is one of the biggest consortia for the deployment of IMS Services. The work will be carried on under the ETSI – GSMA Cooperation Agreement. IMS/EPC interoperability test cases update and extensions will lead to a closer collaboration between TC INT and 3GPP.

## Tasks that cannot be done within the TB and for which the STF support is necessary

It is essential that this work is done in a timely manner in order to provide feedback to 3GPP and to the industry before the starting of GSMA demonstrations and Trials, especially in the context of IMS.

Ensuring the availability of the work by early 2013.

To update the testing framework for mid 2013, the test specification should be ready early 2013.

ETSI members have invested considerable resources in developing the test suite for the past ETSI IMS Plugtests events, and would benefit from using it in these tests

To continue and complete the work previously done by STF 414 (Update of IMS NNI Test Specifications for 3GPP R9, RCS 3.0 and IMS&EPC)

The ETSI members do not have sufficient resources to develop the test specifications completely on their own and with the high quality level which is required.

## Related voluntary activities in the TB

The ETSI Members supporting the creation of the STF are committed to supporting this STF in terms of participation in the STF Steering Group, providing input and review to the STF, providing test bed structures and test tools.

## Outcome from previous funded activities in the same domain

STF394 (Extension of IMS NNI interoperability test descriptions)

Revision of TS 186 011-1/-2 to 3GPP Rel.8 and production of TS 102 901 for RCS Rel.2

Resource: 75 remunerated and 30 voluntary effort days, 45 000€+

STF414 (Update of IMS NNI Test Specifications for 3GPP R9, RCS 3.0 and IMS&EPC)

Revision of TS 186 011-1/-2 to 3GPP Rel.9 and of TS 102 901 to RCS-e and production TS 103 029 (IMS-EPC interworking)

Resource: 80 remunerated and 15 voluntary effort days, 48 000€+

## Consequences if not agreed

Failure to agree to this STF will result in significant delay to the development of these TSs which today can give RCS VoLTE IOT events the right scheduling in order provide feedback to 3GPP and to the industry before the starting of GSMA demonstrations and Trials.  A delay in the development of these test specifications could lead to not being able to perform an IMS interoperability event in 2013 for 3GPP R10, leaving the gap between 3GPP specifications and interoperability events. Without the availability of suitable test specifications, IMS interoperability testing activities will be of little technical commercial or promotion value. In addition to the IMS interoperability event, VoLTE plugtest can be also endangered or at least the quality of results provided by this event when the proposed extension will not be supported.

Part II - Execution of the work

# Technical Bodies and other Organizations involved

## Leading TB

TC INT, Giulio Maggiore

## Other interested ETSI Technical Bodies

3GPP CT1

3GPP CT3

3GPP SA3

3GPP RAN5

ETSI TC MTS

ETSI TC STQ

## Other interested Organizations outside ETSI

GSMA IREG

GSMA RCS

The MSF

# Working method/approach

## Organization of the work

The work can be separated in 8 main tasks:

T1 - Analysis of Impacts of 3GPP Release 10 on existing IMS NNI test specifications:

TS 186 011-1 (Test purposes for IMS NNI Interoperability),

TS 186 011-2 (Test descriptions for IMS NNI Interoperability),

TS 102 901 (IMS NNI interoperability test descriptions for RCS),

TS 103 029 (IMS & EPC Interoperability)

T2 - Update TS 186 011

Part 1 - Test Purposes for IMS NNI Interoperability,

Part 2 - Test Descriptions for IMS NNI Interoperability,

T3 – Update TS 102 901: IMS NNI interoperability Test descriptions for RCS,

T4 – Update TS 103 029: IMS & EPC Interoperability Test Descriptions

T5 – Extend TS 103 029: IMS & EPC Interoperability Test Descriptions to further interfaces

T6 - Develop a set of QoS test extensions to TS 186 011, TS 102 901 and TS 103 029

T7 - Integrate feedback from test houses and the conclusions and results of a validation test planned by ETSI CTI for December 2013

T8 - Support to ETSI CTI by both QoS experts during the validation tests.

## Base documents

| Document | Title | Current Status | Expected date for stable document |
| --- | --- | --- | --- |
| ETSI TS 124 229 Rel. 10 | IP multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3 | Published (V10.8.0) | Further Rel.10 versions expected |
| GSMA RCS 5.0 | Rich Communication Suite 5.0 Advanced Communications; Services and Client Specification; Version 1.0 | Published | - |
| ETSI TS 186 011-1 V.4.1.1 | Test Purposes for IMS NNI Interoperability | Published | - |
| ETSI TS 186 011-2 V.4.1.1 | Test Descriptions for IMS NNI Interoperability | Published | - |
| ETSI TS 102 901 V.2.1.1 | IMS NNI interoperability Test descriptions for RCS | Published | - |
| ETSI TS 103 029 V.3.1.1 | IMS & EPC Interoperability Test Descriptions | Published | - |
| ETSI TR 102 648-1 V1.1.1 (2006-12) | Speech Processing, Transmission and Quality Aspects (STQ); Test Methodologies for ETSI Test Events and Results; Part 1: VoIP Speech Quality Testing | Published |  |
| DTS/INT-00091 TS 103 189 v.0.2.4 | IMS Network Testing (INT); Specification of end-to-end QoS assessment for LTE and RCS Interop Events or Plugtests | TB approved |  |

## Deliverables

| Deliv. | Work Item code Standard number | Working title Scope |
| --- | --- | --- |
| D1 | RTS/INT-00085-1 TS 186 011-1 | IMNS Network Testing (INT); IMS NNI Interoperability Test Specifications. Part 1: Test Purposes and Test Suite Structure for IMS NNI Interoperability |
| D2 | RTS/INT-00085-2 TS 186 011-2 | IMNS Network Testing (INT); IMS NNI Interoperability Test Specifications. Part 2: Test Descriptions for IMS NNI Interoperability |
| D3 | RTS/INT-00086 TS 102 901 | IMS Network Testing (INT); IMS NNI Interoperability Test Specifications; IMS NNI interoperability test descriptions for RCS |
| D4 | RTS/INT-00087 TS 103 029 | IMS Network Testing (INT); IMS & EPC Interoperability test descriptions |
| D5 | DTS/INT-00091 TS 103 189 v.1.1.1 | IMS Network Testing (INT); Specification of end-to-end QoS assessment for LTE and RCS Interop Events or Plugtests |
| D6 | RTS/INT-000xx TS 103 189 v.2.1.1 | IMS Network Testing (INT); Specification of end-to-end QoS assessment for LTE and RCS Interop Events or Plugtests |

## Deliverables schedule:

Start of work	11-02-2013

ToC and scope	19-03-2013	INT#20

Early draft	18-06-2013	INT#21

Stable draft	03-09-2013	INT#22

TB approval	12-12-2013	INT#23

Publication	31-01-2014

For D6:

Start of work	01-10-2013

ToC and scope	01-10-2013

Early draft	10-12-2013

Stable draft	01-02-2014

TB approval	15-02-2014

Publication	31-03-2014

## Work plan, time scale and resources

| N | Task / Milestone / Deliverable | Target date | Testing experts (days) | QoS experts (days) | CTI contrib. (days) |
| --- | --- | --- | --- | --- | --- |
| M0 | Start of work | Feb 2013 |  |
| T0 | Project management, reporting | Feb – Sep 2013 | 5 |  |  |
|  | CTI supervision |  |  |  | 5 |
| T1 | Analysis of impact of 3GPP R10 and RCS5 on existing IMS NNI test specifications |  | 10 |  |  |
| T2 | Update TS 186 011 |  | 15 |  |  |
| T3 | Update TS 102 901 |  | 20 |  |  |
| T4 | Update TS 103 029 |  | 5 |  |  |
| T5 | Extend TS 103 029 |  | 30 |  |  |
| T6 | QoS test extensions to TS 186 011, TS 102 901 and TS 103 029 |  |  | 20 |  |
| T7 | Revision of TS 103 189 | Oct 2013 - Feb 2014 |  | 20 |  |
| T8 | Support of Validation Test | Dec 2013 |  | 6 | 3 |
| M1 | Stable draft for TB review (INT#21) | May 2013 |  |
| M2 | Final draft for TB review (INT#22) | Sep 2013 |  |
| T7 | Consider comments |  | 5 |  |  |
| M3 | Final draft for TB approval (INT#23) | Dec 2013 |  |
| Total | 90 | 46 | 8 |

INT meetings

INT#20	19-21 Mar	Sophia Antipolis FR	first report

INT#21	18-20 Jun	Vienna AT	current drafts

INT#22	03-05 Sep	Sophia Antipolis FR	final drafts for review

INT#23	10-12 Dec	Sophia Antipolis FR	final drafts for approval

STQ meetings

# STQ#42	04-08 Feb	Prague CZ

# STQ#43	10-14 Jun	tbd (proposed Sophia Antipolis)

# STQ#44	14-18 Oct	Lannion FR

## Task and milestone description

Task 1 – Analysis of Impacts of 3GPP Release 10 on existing IMS NNI TS

Analyze the impact of 3GPP Release 10 on existing IMS NNI Test Specifications:

TS 186 011-1 (Test purposes for IMS NNI Interoperability),

TS 186 011-2 (Test descriptions for IMS NNI Interoperability),

TS 102 901 (IMS NNI interoperability test descriptions for RCS),

TS 103 029 (IMS & EPC Interoperability)

Task 2 – Update TS 186 011 TS

Update TS 186 011, parts 1 and 2 to 3GPP Rel 10

Part 1 - Test Purposes for IMS NNI Interoperability,

Part 2 - Test Descriptions for IMS NNI Interoperability,

Task 3 – Update TS 102 901: IMS NNI interoperability Test Descriptions for RCS,

Update TS 102 901 to RCS 5.0

Task 4 – Update TS 103 029: IMS & EPC Interoperability Test Descriptions

Minor updates to TS 103 029 to 3GPP Rel 10

Task 5 – Extend TS 103 029: IMS & EPC Interoperability Test Descriptions

TS 103 029 to cover further interfaces considering comments from interoperability event

Task 6 – QoS test extensions to TS 186 011, TS 102 901 and TS 103 029

Develop the QoS tests and benchmark values or ranges that are to be included in these test specifications. This includes general test conditions, test setup, test methodologies and result representations. The focus will be on conversational voice and video. Impact of different voice bandwidth and different video aspects will be considered.

Task 7 – Revision of TS 103 189

TS 103 189 contains the results of task T6 and is ready for approval in September 2013. This revision will integrate feedback from test houses and the conclusions and results of a validation test planned by ETSI CTI for December 2013.

Task 8 – Support to ETSI CTI during validation tests

ETSI CTI will be supported during the validation tests by the QoS experts

Additional tasks

Attending Technical Body and WG meetings: 	3 working days in total

Drafting non-published documents:	2 working days in total

Milestone 1 – Stable Draft

Presentation of initial drafts of all deliverables and approval of Progress Report by INT#21 (May 2013) plenary. The draft documents must be uploaded by the STF Leader on the TB contributions area of the ETSI Portal before 1 May 2013.

Milestone 2 – Final deliverables for TB review

Review of final drafts of all deliverables and of Final Report by INT#22 (September 2013) plenary. The draft documents must be uploaded by the STF Leader on the TB contributions area of the ETSI Portal before 15 August 2013.

Milestone 3 – TB Approval, STF Final Report

Approval of final drafts of all deliverables and of Final Report by INT#23 (December 2013) plenary. The draft documents must be uploaded by the STF Leader on the TB contributions area of the ETSI Portal before 1 December 2013.

# Required expertise

The following experts are required to perform the work.  The actual number of experts and mix of skills may depend on the actual applications received and will be decided when setting up the STF.

Number of experts required: 2 - 3 plus 2 additional experts for QoS

Relevant expertise required:

Expertise of IMS, SIP Protocol

Expertise in interoperability and conformance testing

Knowledge of RCS services

Expertise of EPC Standards, Diameter

Expertise is required in the QoS area and on wireless technologies

Additional qualification preferred: good knowledge of corresponding standards and connection to network operations and providers deploying LTE to consult with

Part III:	Financial conditions

# Estimated cost

## Manpower cost

| Description | Working days | Rate €/day | Total cost € |
| --- | --- | --- | --- |
| Contracted experts (remunerated) | 72 +36.8 (QoS) | 600 | 65 280 |
| Contracted experts (voluntary) | 18 + 9.2 (QoS) | 0 |  |
| CTI staff from ETSI budget | 0 | 0 |  |
| CTI staff (voluntary) | 8 | 0 |  |
| Total manpower cost | 144 | - | 65 280 |

## Travel Costs

| Description | Cost estimate |
| --- | --- |
| INT#21, INT#22, INT#23, support to ETSI CTI | 5 000 |
| Total cost | 5 000 |

## Other Costs

None

Part IV:	STF performance evaluation criteria

# Key Performance Indicators

Key performance indicators suitable for this kind of STF projects are the following:

Contribution from ETSI Members to STF work

Voluntary work of experts (free of charge or with partial remuneration)

Steering Group meetings (number of participants/duration)

Delegates attending meetings/events related to STF (number of participants/duration)

Direct contribution of delegates (e.g. number of documents/comments/e-mail)

Support to the STF work (e.g., provision of test–beds, organization of workshops, events)

Contributions/presentations to other ETSI TBs

Contributions received from other ETSI TBs

Contribution from STF experts to ETSI work

Contributions presented to TB/WG meetings (number, type, comments received)

Presentations in workshops, conferences, stakeholder meetings

Liaison with other stakeholders

Stakeholder participation in the project (category, business area)

Cooperation with other standardization bodies

Potential interest of new members to join ETSI

Liaison to identify requirements and raise awareness on ETSI deliverables

Comments received on drafts (e.g. on WEB site, mailing lists, etc.)

Quality of deliverables

Approval of deliverables according to schedule

Respect of time scale, with reference to start/end dates in the approved ToR

Quality review by TB

Quality review by ETSI Secretariat

In the course of the activity, the STF Leader will collect the relevant information, as necessary to measure the performance indicators.  The result will be presented in the Final Report.

# Document history

|  | Date | Author | Status | Comments |
| --- | --- | --- | --- | --- |
| 0.1 | 07-08-2012 |  | Draft | First Draft |
| 0.3 | 11-09-2012 | STQ | INT approval | QoS extensions included |
| 0.4 | 17-09-2012 |  | Review | Editorials |
| 0.5 | 19-10-2012 |  | Review | Clarifications, new supporting Members |
| 0.6 | 24-01-2013 | Berrini | Prep. Meet. | Time scale, milestones, synchronization with meeting calendar. |
| 1.0 | 09-08-2013 | Pomy | proposed | STF extension |
| 1.1 | 05-09-2013 | INT | INT#22 approved | Added Task 7, task 8. Extension 15 480 €for approval Board#94 (18-19 September 2013). |

# Comments

Should be 1.0.0 or 0.3.0

Why two deliverables?