|  | ToR STF 507 (TC ITS) |
| --- | --- |
|  | Version: 0.5 |
|  | Author: Sebastian Muller – Date:15 June 2015 |
|  | Last updated by: Alberto Berrini – Date 5 November 2015 |
|  | page 1 of 9 |

Terms of Reference - Specialist Task Force STF 507 
(TC ITS / WG5) - ”Conformance Validation Framework Security Test Specifications of TS 103 097 - Exception Handling”

Summary information

| Approval status | Approved by TC ITS#19 [ITS(15)000129r1] Approved by Board#104. |
| --- | --- |
| Funding | Contracted expert up to 72 working days, including voluntary contribution 20% of total CTI 20 working days (out of budget) Manpower cost: up to 60 days @ 600€/day = 36 000 € + 12 days free of charge |
| Time scale | 19-November 2015 – 1 July 2016 |
| Work Items | RTS/ITS-00534, RTS/ITS-00535, RTS/ITS-00536 |
| Board priority category | Standards enablers/facilitators (e.g. conformance test/interoperability/methodology) Recommendations: use of TTCN and CTI supervision, require average 20% voluntary contribution from Companies sending experts. |
| Notes from Secretariat | There is strong support of ETSI Members with industrial interest in different business areas, that the validation of the Security Conformance Test standards is completed on time and contained all possible tests. So that the STF can start in October 2016. Cost estimate is based upon a detailed analysis of the tasks to be performed and has been reviewed and endorsed by CTI. This estimate includes some margin to take into account the uncertainty on the technical difficulties, in the order of 10-20%. Contracts will be released in phases for the net amount of work estimated. The reserve margin will be used only if there will be proven technical difficulties. |

Part I – Reason for proposing the STF

ITS protocols have been specified and designed to operate correctly across a wide variety of infrastructures worldwide. The risk profile for ITS systems indicates a high impact of these protocols if their design includes a widespread error or fault. This issue provides evidence that successful testing and interoperability are key factors that enable the deployment of these technologies and their successful global introduction.

ETSI Test Specifications cover already ITS Access Layer, Networking Layer and Facility Layer. Security Layer is covered only in the part of sending behaviour. In view of ITS deployment it is essential to provide standardized test specifications for the receiving and exceptional behaviour in Security Layer and thus completing the coverage of test specifications for the ITS layers.

STF481 produced about 70 mandatory tests, which cover the sending behaviour of the ITS station. All these test purposes have been implemented and validated. The STF also produced 160 optional test purposes for receiving and exceptional behaviour, but only 36 of them has been implemented due to time limit.

During the ITS Interoperability Plugtests, end 2014, many companies participated in test sessions with Security Conformance Test Suite, presented by ETSI, passed all mandatory tests of sending behaviour and were very interested to continue test sessions with receiving and exceptional behaviour. It is very important to extend the ETSI Security Test Specifications by additional tests, covering receiving and exceptional behaviours of ITS stations.

As a by-product, the proposed STF improves the quality of the base specifications. A change request mechanism will be put in place to allow the timely feedback on revealed bugs and inconsistencies of base specifications into the TC ITS standardization process, and thus achieve optimized base specifications.

# Rationale

In 2010, TC ITS started together with ETSI CTI a STF project funded by the EC/EFTA to produce conformance test specifications for the Release 1 of TC ITS CAM, DENM, BTP, GN and GN6 protocols. In 2011/2012 a prototype test system (so called Conformance Validation Framework) was designed, built and validated (see http://portal.etsi.org/stfs/STF_HomePages/STF424/STF424.asp). The security layer test suite containing mandatory tests of sending behaviour, was built and validated at the end of 2014,

The Conformance Validation Framework is a reference implementation and available to all ITS stakeholders. The Conformance Validation Framework enables vendors to assess the level of compliance of their equipment and the Conformance Validation Framework can be used in support of certification schemes. In addition, with its high degree of extensibility, it can be used for company internal testing.

Since the closure of STF481, the Conformance Validation Framework has been maintained to align to various base standard revisions in order to provide always tests, which are up to date.

This STF proposal is a further action to extend the ITS Conformance Validation Framework with tests covering receiving and exceptional behaviours of ITS stations based on TS 103 097.

# Objective

The objective of this STF proposal is to revise the PICS document TS 103 096-1, the TSS & TP document TS 103 096-2 and the ATS document TS 103 096-3 to include tests of receiving and exceptional behaviour of ITS stations based on TS 103 097.

The revision of PICS, TSS&TP and ATS documents shall be limited to the test groups SEC/ITS-S/ S-DATA and SEC/ITS-S/R-DATA. Not all other groups are included in the objective of this STF proposal.

All the delivered tests will be optional, and will be used as input to TS 102 941 base specification.

| Root | Group | Group | category |
| --- | --- | --- | --- |
| SEC | CA | ENR/AUTH | Normal behaviour |
|  |  |  | Exceptional behaviour |
|  | EA | ENR | Normal behaviour |
|  |  |  | Exceptional behaviour |
|  | AA | AUTH | Normal behaviour |
|  |  |  | Exceptional behaviour |
|  | ITS-S | ENR | Normal behaviour |
|  |  |  | Exceptional behaviour |
|  |  | AUTH | Normal behaviour |
|  |  |  | Exceptional behaviour |
|  |  | S-DATA | Normal behaviour |
|  |  |  | Receiving and exceptional behaviour |
|  |  | R-DATA | Normal behaviour |
|  |  |  | Receiving and exceptional behaviour |

Furthermore, the objective of this present STF proposal is to validate the test specification against at least two security implementations.

# Relation with ETSI strategy and priorities

This action supports the ETSI Long Term Strategy item(s) to:

create high quality standards for global use and with low time-to-market.

establish leadership in key areas impacting members' future activities

This action has a priority category of:

Standards enablers/facilitators (conformance testing, interoperability, methodology)

# Context of the proposal

## ETSI Members support

| ETSI Member | Supporting delegate | Motivation |
| --- | --- | --- |
| HITACHI | Lan Lin | Test tooling support for industry |
| Kapsch | Tijink Jasja | Support quality-built test standards that reflect the latest developments of the base security standards |
| RENAULT | Brigitte LONC | To use the test tool for product releases |
| SIEMENS | Herbert Fuereder | SIEMENS AG is very interested to have the conformance tests extended with a security test suite. We use the conformance test platform to evaluate new releases of our C2X products |
| ITRI | Huei-Ru Tseng | Test tooling support for industry |

## Market impact

Interoperability is a key factor that enables the use of new technologies and provides all benefits attached to them, such as competitiveness, innovation and reliability.

ITS technologies are becoming more and more complex, collaborative and interdependent. Furthermore, ITS systems are often specified by multiple standards from different standardization development organisations (SDOs). These factors potentially lead to non-interoperability standards. The development of products that rely on non-interoperable standards can eventually result in fragmented markets, all of which can impact trustability.

Various measures can significantly improve the reliability and interoperability of complex systems such as ITS: The development of test specifications for conformance and interoperability can be coupled with validation activities, such as building prototype test systems. Likewise, the prototype test systems can be used at interoperability events. Consequently, the project contributes to the effort of testing and validation ITS systems with the goal to bring the ITS systems to a stage where end users trust the services provided.

## Tasks that cannot be done within the TB and for which the STF support is necessary

Experience with the development of other standards has shown that involvement of experts on conformance and interoperability testing of protocols requires highly specialised knowledge in testing methodology. The generation of this kind of specifications requires significant concentrated effort that can be done in this case by experts provided on a funded basis. Hence, the involvement of testing experts is needed in order to assure timely completion and high quality of the Test Specifications. The experts will use dedicated software tools available at ETSI. Test adapter development and test suite validation are expert tasks, which cannot be provided by a TB.

## Related voluntary activities in the TB

Delegates within the TC will review the deliverables and deal with the CRs on base specifications that that this action will produce.

## Outcome from previous funded activities in the same domain

TC ITS has benefited of STF support in this domain during the last 5 years:

TC ITS WG2: STF398 (2010) 72 000

TC ITS WG1/3: STF405 (2010-2012) EC/EFTA 354 000 €

TC ITS WG1/3: STF424 (2010-2012) EC/EFTA 246 900 €

TC ITS WG1/3: STF449 (2013) ETSI 68 000 €

TC ITS WG5: STF452 (2013/2014) ETSI 77 400 €

TC ITS WG1/3: STF462 (2013/2014) ETSI 63 200 €

TC ITS WG5: STF481 (2014/2015) ETSI 128 000 €

TC ITS WG1/3: STF484 (2014/2015) ETSI 51 200 €

## Consequences if not agreed

The production of test specifications as described in the present document is key to the testing and potential certification activities that should assure the interoperability of ITS equipment. Such devices are required to have high levels of interoperability if the safety on road is to be kept at the highest level. The non-availability of such standards may cause problems of interoperability.

Part II - Execution of the work

# Technical Bodies and other Organizations involved

## Leading TB

The leading WG is TC ITS WG5.

## Other interested ETSI Technical Bodies

NA

## Other interested Organizations outside ETSI

Other interested parties, but not limited to, are C2C CC, ERTICO, C-ITS Platform

# Working method/approach

## Organization of the work

The work will be done in two waves. In the first wave, the test specifications will be updated and developed. In the second wave, the test specifications will be validated against at least two devices.

## Base documents

| Document | Title | Current Status | Expected date for stable document |
| --- | --- | --- | --- |
| ETSI TS 102 940 V1.1.6 | Intelligent Transport Systems (ITS); Security; Security Architecture and Management | WG approved | Publication expected in January no stable document required for the present work |
| ETSI TS 102 941 V1.1.4 | Intelligent Transport Systems (ITS); Security; Trust and Privacy Management | Early draft | no stable document required for the present work |
| ETSI TS 103 096-1 V1.2.1 (RTS/ITS-00528) | Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 1: Protocol Implementation Conformance Statement (PICS) | Published |  |
| ETSI TS 103 096-2 V1.2.1 (RTS/ITS-00529) | Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 2: Test Suite Structure and Test Purposes (TSS & TP) | Published |  |
| ETSI TS 103 096-3 V1.2.1 (RTS/ITS-00530) | Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT) | Published |  |
| ETSI TS 103 097 V1.2.1 (RTS/ITS-00531) | Intelligent Transport Systems (ITS); Security; Security header and certificate formats | TB approval | October 2015 |

## Deliverables

| Deliv. | Work Item code Standard number | Working title Scope |
| --- | --- | --- |
| D1 | RTS/ITS-00534 TS 103 096-1 | Title: Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 1: Protocol Implementation Conformance Statement (PICS) Scope: Update the PICS regarding the receiving and exceptional behaviour of ITS stations defined in TS 102 941 and TS 103 097. |
| D2 | RTS/ITS-00535 TS 103 096-2 | Title: Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 2: Test Suite Structure and Test Purposes (TSS & TP) Scope: Update the TSS&TP regarding the receiving and exceptional behaviour of ITS stations defined in TS 102 941 and TS 103 097. |
| D3 | RTS/ITS-00536 TS 103 096-3 | Title: Intelligent Transport Systems (ITS); Testing; Conformance test specification for ITS Security; Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT) Scope: Develop a test suite for tests of receiving and exceptional behaviour of ITS stations defined in TS 102 941 and TS 103 097. |

## Deliverables schedule:

RTS/ITS-00528, RTS/ITS-00529, RTS/ITS-00530: Security Testing PICS, TSS&TP and ATS

Start of work	Nov-2015

ToC and scope	Nov-2015

Early draft	Dec-2015

Stable draft TPs for WG review	13-Jan-2016	WG5#38

Stable draft PICS and ATS for WG review	13-Apr-2016		WG5#39

TB approval		1-Jul-2016	ITS#23

Publication	1-Aug-2016

## Work plan, time scale and resources

| N | Task / Milestone / Deliverable | From | To | Funded experts (max days) | CTI experts (days) |
| --- | --- | --- | --- | --- | --- |
| Wave 1 – Test standards TS 103 096-1, TS 103 096-2, TS 103 096-3 |
| M1.0 | Start of work | 15-Nov-2015 |  |  |
| T0 | Project management | 15-Nov 2015 | Jul 2016 |  | 5 |
| T1 | Development of TSS&TP | 15-Nov-2015 | Jan 2016 | 10 |  |
| M1.1 | Stable Draft TPs for WG review (WG5#38) | 13-Jan-2016 |  |  |
| T2 | Development of TTCN-3 scripts | Dec 2015 | Apr 2016 | 40 |  |
| M1.2 | Stable Draft PICS and ATS for WG review (WG5#39) | 13-Apr-2016 |  |  |
| T3 | Quality Check of Test Standards | Apr 2016 |  | 3 |
| T4 | Include WG comments, if any | May 2016 |  | 1 |
| M1.3 | Final draft for TB approval (ITS#23) | 1-Jul-2016 |  |  |
| M1.4 | Publication | 1-Aug-2016 |  |  |
| Total Wave 1 | 50 | 10 |

| N | Task / Milestone / Deliverable | From | To | Funded experts (max days) | CTI experts (days) |
| --- | --- | --- | --- | --- | --- |
| Wave 2 – Validation of TS 103 096-1, TS 103 096-2, TS 103 096-3 against at least 2 devices |
| M2.0 | Start of work | Jan 2016 |  |  |
| T6 | Project management | Jan 2016 | Mar 2016 |  | 7 |
| T7 | Validation | Jan 2016 | Mar 2016 | 16 |  |
| M2.1 | Correction of TS 103 096-1, TS 103 096-2, TS 103 096-3 | Mar 2016 | Jun 2016 | 6 | 3 |
| Total Wave 2 | 22 | 10 |

Note: effort estimate includes margin to take into account uncertainty on the technical difficulties.  Contracts will be released in phases, under the supervision of ITS WG5 and CTI, in order to ensure that only the amount of resources that are actually required will be spent.  The ETSI Secretariat will report on the actual progress and expenditure to each Board meeting.

## Task description

Task 0 and Task 6 – Project Management and Code Review

Coordination, communication, reporting and leading of activities. In addition, code review of the project.

Task 1 – Development of TSS&TP

Update TSS&TP document to add tests covering the receiving and exceptional behaviour of ITS stations. This applies to test groups SEC/ITS-S/ S-DATA and SEC/ITS-S/ R-DATA only.

Task 2 – Development of TTCN-3 scripts

Continue to develop the TTCN-3 part of the ATS test specifications. This applies to test groups SEC/ITS-S/ S-DATA and SEC/ITS-S/ R-DATA only.

Task 3 – Quality Check of Test Standards

Peer review of PICS, TSS&TP and ATS documents to ensure technical quality.

Task 4 – Include WG comments, if any

Modify documents PICS, TSS&TP and ATS documents according to received comments. In case no comments are received, this task is not relevant.

Task 7 – Validation

This STF will provide level 2 validation as shown in the table below. The ITS Conformance Validation Framework shall be validated against a minimum of at least 2 SUTs. These SUTs need to be available and installed on computers at ETSI premises. The responsibilities shown in the table below shall be shared by the STF team. In addition and beyond the STF effort, it is expected to get documentation and support from the company providing the SUTs on any issues that may arise. This support shall be limited to reasonable effort.

Table 1: Responsibilities of validation

| Basic Validation (Level 1) | Strong Validation (Level 2) |
| --- | --- |
| Provision of TTCN-3 analyser/compilers |  |
| Compilation of the test suite on at least 2 TTCN-3 compilers |  |
| Reporting of errors in the tools |  |
| Reporting of errors in the ATS |  |
| Updating of ATS |  |
| Compilation of validation report |  |
|  | Extending and maintaining of the ITS Conformance Validation Framework |
|  | Provision and installation of SUT(s) |
|  | Execution of the tests |
|  | Reporting of errors in the ITS Conformance Validation Framework |
|  | Validation of test verdicts |

# Required expertise

2 experts to ensure the following mix of skills:

expert knowledge of TS 102 941, TS 103 097 and IEEE1609.2;

expert knowledge of TTCN-3 (ES 201 873);

good experience of conformance and/or interoperability testing;

expert knowledge in codec and adaptation layer development;

expert knowledge in PKI pilot setups

expert knowledge of ITS Security implementations

Part III:	Financial conditions

# Estimated cost

## Manpower cost

| Description | Working days | Rate €/day | Total cost up to € |
| --- | --- | --- | --- |
| Contracted experts (remunerated) | 60 | 600 | 36 000 |
| Contracted experts (voluntary) | 12 | NA | NA |
| CTI staff (voluntary) | 23 | NA | NA |
| Total manpower cost | 95 |  | 36 000 |

## Travel Costs

NA

## Other Costs

NA

Part IV:	STF performance evaluation criteria

# Key Performance Indicators

Contribution from the ETSI Members

Provision of an ITS device for validation

Reporting to meetings on any base spec issues, if any

Interest from stakeholders other than ETSI Members

Provision of an ITS device for validation

Quality of deliverables

Implementation of TTCN-3 scripts for all Test Purposes

Approval of deliverables from the Reference TB according to schedule

Respect of time scale, with reference to start/end dates in the approved ToR

In the course of the activity, the STF Leader will collect the relevant information, as necessary to measure the performance indicators.  The result will be presented in the Final Report.

# Document history

|  | Date | Author | Status | Comments (main issues) |
| --- | --- | --- | --- | --- |
| 0.1 | 28-05-15 | Sebastian Muller | Draft | Draft of ToR |
| 0.2 | 10-06-15 | Sebastian Muller | TC approved | Comments from ITSWG5#36 incorporated Approved by TC ITS#19 [ITS(15)000129r1] |
| 0.3 | 10-07-15 | Sebastian Muller | TC approved | Comments from Kevin Holly incorporated |
| 0.4 | 04-08-15 | Sebastian Muller | Board approved | WIs added |
| 0.5 | 05-11-15 | Alberto Berrini | Prep. Meet. | Updated time scale |